## Slide 1
Upper Hudson
Lower Hudson

## Slide 2: NYC “Sewershed”

## Slide 3: Combined Sewer System & Combined Sewer Overflows (CSO)

## Slide 4: CSO Outfall Map
New York City has 450+ CSO outfalls from the Harlem River to the Gowanus Canal
Combined sewer systems make up ~60% of New York City's sewershed
CSOs discharge over 20 billion gallons of polluted water into NYC waterways each year
Credit: SWIM Coalition / Open Sewer Atlas

## Slide 5: Municipal Separate Storm Sewer System (MS4)

## Slide 6: Citizens’ Water Quality Testing Program
= Sampling site; includes boat launches and other water access points
= CWQTP laboratory

## Slide 7: Enterococci as fecal indicator bacteria
Found in fecal matter of warm-blooded animals
Strong correlation between swimmer illness and enterococci levels (although entero probably don’t cause illness)
Survive in salt water
Generally not found in environment
Considerations
Killed by UV
Somewhat associated with particulate matter
Boehm AB, Sassoubre LM. Enterococci as Indicators of Environmental Fecal Contamination. 2014

## Slide 8: IDEXX Enterolert method for detecting Enterococcus
Results in 24 hours
Enumerates <10 – 24,190 enterococci per 100 mL brackish water
EPA-approved method
Enzyme cleaves reagent, producing fluorescent molecule
Reagent: modified carbohydrate
Enzyme found in enterococci
Wells containing enterococci fluoresce

## Slide 9: HyServe Compact Dry ETC method
Results in 24 hours
Lower equipment cost
Enumerates 100-30,000 enterococci per 100 ml
Not EPA-approved
Media contains antibiotics that kill bacteria other than Enterococcus
Enterococcus colony.
X-glucoside in media is cleaved by Enterococcus enzyme that produces blue product

## Slide 10: Aseptic Technique
Sterile work surface
uncluttered work area
wipe down work surface with bleach or 70% ethanol
Personal hygiene & protective gear
wash hands past wrists before/after lab work
always wear lab gloves while working in lab
do not touch face, body, unsterile surfaces/items with gloves
Sterile Handling
only use pipettes once to avoid cross-contamination
pipette should transfer from one vessel to the next without touching other surfaces
only uncover a vessel when you are ready to use it and replace cap as soon as possible

## Slide 11
by NYC DEP

## Slide 13
NYC DOH Enterococcus Standards (for swimming) |  | 
Green: <35 MPN--acceptable |  | 
Yellow: 35-104 MPN--unacceptable if levels persist |  | 
Red: >104 MPN--unacceptable |  | 

## Slide 15
*A geometric mean is a weighted average that is less sensitive to outliers than an arithmetic mean
*

## Slide 16
Notes: maps taken from 2017 Harbor Survey Monitoring Stations

## Slide 17
<100 count/100mL
100 - 200
201 - 2000
>2000
Fecal Coliform Bacteria

## Slide 18
http://blog.uvm.edu/kstepenu/files/2016/11/Bact-Present_XV.pdf
http://norwalkriver.org/wpcontent/uploads/2014/11/NR-winter-report-Oct-2010-through-April-2011.pdf

## Slide 19
San Antonio River Authority: https://www.sara-tx.org/apps/bacteria_charts/ecoli_chart_logrithm.php
http://blog.uvm.edu/kstepenu/files/2016/11/Bact-Present_XV.pdf

## Slide 20
https://www.riverkeeper.org/water-quality/hudson-river/nyc-hudson-bergen/newtown-creek-metropolitan-ave-bridge/